## Slide 1: ROS-Industrial Basic Developer’s Training Class
Shaun Edwards
Sr. Research Engineer
Southwest Research Institute
4 June 2014

## Slide 2: Overview

## Slide 3: Overview Presentation
See “What Can ROS-I Do Today?” presentation

## Slide 4: Introduction to ROS-I (Users & Developers)

## Slide 5: Outline
Community
Wiki Documentation
Getting Help
Installing ROS

## Slide 6: Objectives
Learn how to participate and interact in the community
Understanding of ROS/ROS-I wiki
Know where and how to ask for help
Be able to install ROS-I from binary and source
Entertain you 

## Slide 7: ROS-I is a Community
Members: users, developers, researchers, bystanders, star trek fans(not star wars)
Resources:
  Wiki – http://ros.org/wiki/Industrial
  Email– http://groups.google.com/group/swri-ros-pkg-dev
  Forums – http://answers.ros.org/questions/
  Repos (migrating to Github)
    http://code.google.com/p/swri-ros-pkg/
    http://github.com/organizations/ros-industrial

## Slide 8: ROS-I is a Community
Resources(cont):
  Twitter - https://twitter.com/ROSIndustrial
  Blog - http://rosindustrial.tumblr.com/
  YouTube channel - http://www.youtube.com/channel/UCXyGVRiCwUMc1gav-G7z2ew

## Slide 9: ROS-I is a Community
Community is managed, organized, and monitored by SwRI & RIC
  Monitored: Wiki, Group emails, Forums
  Access Controlled: Repos, Twitter, Blogs, YouTube channel

## Slide 10: ROS-I Wiki
A Wiki is a website which allows people to add, modify, or delete the content via a web browser usually using a simplified markup language or a rich-text editor. (http://en.wikipedia.org/wiki/Wiki)
It’s a Wiki, YOU can edit it!

## Slide 11: ROS-I Wiki
The ROS/ROS-I wiki contains documentation for users(focus) and developers
Documentation organized according to packages & stacks/meta-packages

## Slide 12: ROS-I Wiki
Users
  Overview
  Tutorials
Developers
Architecture/Design
Code API
Dependencies
Bug Tracker
  Typical Content

## Slide 13: Wiki Walkthroughs
ROS-I Wiki(follow): http://ros.org/wiki/Industrial
ROS-I Package Wiki (simple_message)(follow): http://ros.org/wiki/simple_message

## Slide 14: Getting Help
ROS Answers(follow): http://answers.ros.org/questions/
Developers List: http://groups.google.com/group/swri-ros-pkg-dev
  Join here: https://groups.google.com/group/swri-ros-pkg-dev/boxsubscribe

## Slide 15: Getting Help
Submitting Bugs (not for any code I have written)
  Google Code: http://code.google.com/p/swri-ros-pkg/issues/list
  Github Code: http://github.com/organizations/ros-industrial/dashboard/issues
  Good bug submission:
    Setup, Steps to reproduce, Expected Results
  Best bug submission ever:
    Good submission + Test Code

## Slide 16: Getting Help
Call Us(Consortium Members Only)
  Paul Hvass W: 210-522-5823, Home: ….
Collaboration
  Generally open source
Consulting
  Whatever you want
  Various IP terms

## Slide 17: Installing ROS-I
Binary (using apt-get)
Recommended for users
Stable
Easy
Source (repos)
Required for developers
Google Code
Github (future)
Harder
Unstable*
Latest capability

## Slide 18: Binary Install
Command line: sudo apt-get install <package>
  ros-<version>-industrial-core
  ros-<version>-industrial-desktop
  ros-<version>-abb
  ros-<version>-motoman
  ros-<version>-fanuc
  ros-<version>-adept
  ros-<version>-universal-robotics

## Slide 19: Source Install
Wiki instructions(follow): http://ros.org/wiki/Industrial/Install
  Repository structure
  Experimental stacks/meta-packages
  Google Code vs. Github

## Slide 20: Source Install (SVN)
Install latest Hydro Industrial Core(example)
  Go to the wiki page for the industrial core stack/metapackage.
  Verify the required dependencies are installed on your system (exercise)
  Download the hydro version of the package to the current directory
  Build the stack

## Slide 21: Source Install (Git)
Install a patched version of Robot Models Tutorials (example)
  Go to the ROS-Industrial github main page
  Find the Git link to the robot_models_tutorials repo (it's a fork of the formal ros repo)
  Move to the stack directory, and build the stack

## Slide 22: Exercise
Exercise 4.1(follow) - https://aeswiki.datasys.swri.edu/rositraining/Exercises/4.1

## Slide 23: ROS-I - Simple Message Layer (Core Developers)

## Slide 24: Outline
Overall Architecture
Simple Message Package Overview
Messages and Connections
Managers and Handlers
Library Linking

## Slide 25: Objectives
Understand the top-level ROS-I architecture
Be able to develop ROS-I simple message client/server applications
Understand how the simple message library can be used to bridge ROS messages to simple devices

## Slide 26: Top Level Architecture
Notes: Talk about different layers
Identify ROS-I App & Gui as future
Standard nodes are shown
Configuration data
Availability of ROS ecosystem, move it, and ros gui

## Slide 27: Simple Message Detail
Bridge layer between ROS and Robot Controllers

## Slide 28: Simple Message Package
Package Overview(follow): http://ros.org/wiki/simple_message
New Typed Messages (Post Hydro)
  Joint Trajectory Pt Full (mimics ROS JointTrajectoryPoint) http://ros.org/doc/api/trajectory_msgs/html/msg/JointTrajectoryPoint.html
  Robot Status (mimics ROS-I Robot Status) http://ros.org/doc/hydro/api/industrial_msgs/html/msg/RobotStatus.html
Notes: Motivation
Simple Message
Typed Messages
  joint
  joint traj pt full
  joint traj pt
  robot status
Simple Message Connections
  TCP Client/Servers
  UDP Client/Servers (experimental)

## Slide 29: Talker/Listener
Create 2 nodes, talker and listener
Send simple messages between nodes (NOT ROS messages)
Talker
Listener
Joint Simple
Message (request)
Joint Simple
Message (response)

## Slide 30: Create an Eclipse Project
Make eclipse project files
Import project into eclipse
Enjoy modern IDE features like code completion, syntax checking, etc…
Do not check project files into repos (they aren’t portable)

## Slide 31: Talker Node
// Initialize ROS node "sm_talker"
ros::init(argc, argv, "sm_talker");
// Required to start timers for non-node ROS use.
ros::Time::init();
// Little message to know she's started
ROS_INFO_STREAM("STARTING SM_TALKER");
// Create a TCP client connection to TCP_PORT on LOCAL_HOST (see common.h)
TcpClient client;
client.init(LOCAL_HOST, TCP_PORT);
while(!client.isConnected())
{
ROS_INFO_STREAM("Trying to connect to server");
client.makeConnect();
ros::Duration(0.5).sleep();
}
int seq = 0;
<continued>
while(client.isConnected())
{
// Create a message of type JointMessage and corresponding simple message
JointMessage jmReq;
SimpleMessage req, reply;
seq++;
jmReq.setSequence(seq);
jmReq.toRequest(req);
ROS_INFO_STREAM("Sending sequence number: " << seq);
client.sendAndReceiveMsg(req, reply);
ROS_INFO_STREAM("Received reply code: " << reply.getReplyCode());
ros::Duration(1.0).sleep();
}

## Slide 32: Listener Node
// Initialize ROS node "sm_talker" ros::init(argc, argv, "sm_listener"); // Required to start timers for non-node ROS use. ros::Time::init(); // Little message to know she's started ROS_INFO_STREAM("STARTING SM_LISTENER"); // Create a TCP server connection on TCP_PORT (see common.h) TcpServer server; server.init(TCP_PORT); while(!server.isConnected()) { ROS_INFO_STREAM("Trying to connect to client"); server.makeConnect(); ros::Duration(0.5).sleep(); } while(server.isConnected()) { // Create a message of type JointMessage JointMessage jmReq, jmReply; SimpleMessage req, reply; ROS_INFO_STREAM("Waiting for client request"); server.receiveMsg(req);
if( req.getMessageType() == jmReq.getMessageType() ) { if( req.getCommType() == CommTypes::SERVICE_REQUEST ) { jmReq.init(req); ROS_INFO_STREAM("Received sequence number: " << jmReq.getSequence()); jmReply.toReply(reply, ReplyTypes::SUCCESS); server.sendMsg(reply); ROS_INFO_STREAM("Sending reply code: " << reply.getReplyCode()); } else { ROS_ERROR_STREAM("Unexpected comm type: " << req.getCommType()); } } else { ROS_ERROR_STREAM("Unexpected message type: " << req.getMessageType()); } }

## Slide 33: Exercise
Exercise 4.2(Part 1) - https://aeswiki.datasys.swri.edu/rositraining/Exercises/4.2

## Slide 34: Message Manager/Handler
Message manager/handlers simplify relaying simple messages (similar to ROS msg callbacks)
Allows multiple data streams to use the same connection

## Slide 35: Library Linking
Simple Message compiled as a library for inclusion in other packages
  2 versions compiled (normal, byte swapped)
Linking to Simple Message library (non-standard)
  Example: http://ros.org/wiki/simple_message#Library_Linking

## Slide 36: Message Handler
// Handler class defined specifically for this example class MyHandler : public MessageHandler { // since this class defines a different init(), this helps find the base-class init() using MessageHandler::init; public: bool init(SmplMsgConnection* connection) { return this->init(StandardMsgTypes::JOINT, connection); } private: bool internalCB(industrial::simple_message::SimpleMessage & in) { bool rtn = false; JointMessage jm; SimpleMessage msg; if (jm.init(in)) { ROS_INFO_STREAM("Received sequence number: " << jm.getSequence());
if (jm.toReply(msg, ReplyTypes::SUCCESS)) { if (this->getConnection()->sendMsg(msg)) { ROS_INFO_STREAM("Sending reply code: " << msg.getReplyCode()); rtn = true; } else { ROS_ERROR("Failed to send joint message return"); rtn = false; } } else { ROS_ERROR("Failed to generate joint reply message"); rtn = false; } } else { ROS_ERROR("Failed to initialize joint message"); rtn = false; } return rtn; } };

## Slide 37: Manager
// Initialize ROS node "sm_talker" ros::init(argc, argv, "sm_listener"); // Required to start timers for non-node ROS use. ros::Time::init(); // Little message to know she's started ROS_INFO_STREAM("STARTING SM_MANAGER");
TcpServer server; server.init(TCP_PORT); MessageManager manager; MyHandler handler; manager.init(&server); handler.init(&server); manager.add(&handler); manager.spin();

## Slide 38: Exercise
Exercise 4.2(Part 2) - https://aeswiki.datasys.swri.edu/rositraining/Exercises/4.2

## Slide 39: ROS-I - Interface Layer (Core Developers)

## Slide 40: Outline
Industrial Robot Driver Specification
Industrial Messages
Industrial Robot Clients
Industrial Robot Simulator
Joint Trajectory Filters (experimental) – Post Hydro

## Slide 41: Objectives
Understand the motivation and function of the ROS-Industrial Driver Specification
Understand how to use of the industrial robot clients as standard nodes for talking to robot controllers
Understand how to use the industrial robot simulator
Awareness of the joint trajectory filter package

## Slide 42: Simple Detail
Bridge layer between simple message and high level software

## Slide 43: ROS-Industrial Specification
ROS-I Wiki(follow): http://ros.org/wiki/Industrial/Industrial_Robot_Driver_Spec
Notes: Motivation
Minimal
Full
Hardware Compatibility
Future

## Slide 44: Industrial Messages
ROS-I Wiki(follow): http://ros.org/wiki/industrial_msgs
Notes: Robot status
Motion command service
JointTrajectory
JointStates

## Slide 45: Industrial Robot Clients
ROS-I Wiki: http://ros.org/wiki/industrial_robot_client
3 Types of nodes
  Motion (command joint motion)
    Streaming & download
  State (joint positions and status)
  Joint Trajectory Action (Follow joint trajectory action server)
Motion
Node
State
Node
Action
Node
Notes: Client nodes adhere to the ROS-I spec

## Slide 46: Industrial Robot Simulator
Different from MoveIt Simulator
ROS-I Wiki: http://ros.org/wiki/industrial_robot_simulator
Simulates both robot motion and state nodes (i.e. adheres to spec)
Allows quick development without hardware
Action
Node
Sim
Node

## Slide 47: Joint Trajectory Filters
Experimental (Post Hydro)
Every moveit/arm navigation package has a joint_limits.yaml. See: http://ros.org/wiki/trajectory_filters
ROS-I Wiki (follow): http://ros.org/wiki/industrial_trajectory_filters
Very useful for smoothing out and improving joint motion.

## Slide 48: Introduction to Using ROS-I (app Developers)

## Slide 49: Outline
Top Level Architecture
Application Layer
GUI Layer
Common Application Tasks

## Slide 50: Objectives
Understand the various ways to create application level programs
Understand the interface layer(s)
Understand the possibilities
Steps to build up to an application

## Slide 51: Top Level Architecture
Notes: Application layer
Joint Trajectory action interface/ROS-I spec interface

## Slide 52: Application Layer
ROS Layer
  Anything you can imagine
MoveIt Layer
  Planning
  Kinematics
  Pick & Place
  Workspace evaluation
ROS-I Layer (Future)
  Process based planner
  Industrial state machines

## Slide 53: GUI Layer
ROS GUI
  Qt based GUI
    Powerful
    Widget based
    Cross platform (although ROS isn’t)
ROS-I GUI (Future)
  Generic pendant
  Standard industrial UI
  Industrial Widgets

## Slide 54: Applications Building
Create MoveIt configuration for your application
Verify configuration with physical robot cell (exercise 4.3)
Tweak motion to meet your needs (exercise 4.4)
Build your application code (application specific)
Build GUI interface (application specific)

## Slide 55: Machine Tending Application
Robot, CNC, & Caging
Verify robot and physical layout
Fast motion for large moves, fine motion for interfacing with external equipment
Create industry standard state machine (start, stop, fault reset interface)
Create GUI that has buttons for changing modes, error logs, visualization.

## Slide 56: Robot Package Verification
Exercise 4.3 https://aeswiki.datasys.swri.edu/rositraining/Exercises/4.3

## Slide 57: Improving Robot Motion
Exercise 4.4 https://aeswiki.datasys.swri.edu/rositraining/Exercises/4.4

## Slide 58: Future ROS-I Development

## Slide 59: Outline
What the Future Holds
Please Share Your Ideas

## Slide 60: Objectives
Tell you where we are going
Ask you where you want us to go

## Slide 61: What's next?
Catkin
Github migration
Flexible robot IO control
Improved drivers (vendor supported)

## Slide 62: Process Based Planners

## Slide 63: Standard GUI

## Slide 64: Code Metrics/Unit Tests
Jenkins continuous integration

## Slide 65: Robot Task Description Format
XML file format for describing arbitrary motion
Expressive enough for high/low density waypoints
Encapsulates process data

## Slide 66: Roadmap
ROS-I Wiki (follow): http://ros.org/wiki/Industrial/Roadmap

## Slide 67: What do YOU want?

## Slide 68: Introduction to Perception

## Slide 69: Outline
Explanation of the Perception Tools Available in ROS
Kinect Introduction

## Slide 70: Objectives
Cursory understanding of the perception tools
Experience with Kinect data and tools

## Slide 71: Example: Pick & Place

## Slide 72: Perception Libraries
Point Cloud Library (PCL) - http://pointclouds.org/
  Focused on 3D Range(Colorized) data
http://pointclouds.org

## Slide 73: Perception Libraries
Open Computer Vision Library (OpenCv) - http://opencv.org/
  Focused on 2D images
  2D Image processing
  Video
  Sensor calibration
  2D features
  GUI
  GPU acceleration
http://opencv.org

## Slide 74: ROS Bridges
OpenCV & PCL are external libraries
“Bridges” are created to adapt the libraries to the ROS architecture
  OpenCV: http://ros.org/wiki/vision_opencv
  PCL: http://ros.org/wiki/pcl_ros
    Standard Nodes: http://ros.org/wiki/pcl_ros#ROS_nodelets

## Slide 75: Many More Libraries
Many more libraries in the ROS Ecosystem
  AR Tracker - http://www.ros.org/wiki/ar_track_alvar
  Object Recognition - http://www.ros.org/wiki/object_recognition
  Robot Self Filter - http://www.ros.org/wiki/robot_self_filter
  Let me Google that for you  - http://bit.ly/12PebaA

## Slide 76: Exercise
Exercise 4.5 - https://aeswiki.datasys.swri.edu/rositraining/Exercises/4.5

## Slide 77: Contact Information
Shaun Edwards Senior Research Engineer
Southwest Research Institute
6220 Culebra Rd.
San Antonio, TX 78251 US
Phone: 210-522-3277 Email: sedwards@swri.org
www.rosindustrial.org
www.ros.org/wiki/Industrial