## Slide 1: ROS-Industrial Basic Developer’s Training Class
Dan Solomon
Research Engineer
Southwest Research Institute
May 2014

## Slide 2: Outline
Services
Actions
Launch Files
TF
URDF
Debugging

## Slide 3: Services

## Slide 4: Services: Overview
Services are like a function calls
Each service made up of 2 messages:
  Request, sent by client, received by server
  Response, generated by server, sent to client
Service is defined in plain text format
Supports basic types, and predefined msg types
Call to service blocks in client
  Code will wait for service call to complete before continuing

## Slide 5: Services: Lesson 2.1
Create custom service definition
Create service server
Create service client
int64 a
int64 b
---
int64 sum
bool add(AddTwoInts::Request &req, AddTwoInts::Response &res) {
res.sum = req.a + req.b;
return true;
}
ros::ServiceServer service = n.advertiseService("add_two_ints", add);
Ros::NodeHandle nh;
ros::ServiceClient client = nh.serviceClient<AddTwoInts>("add_two_ints");
AddTwoInts srv;
srv.request.a = 4;
srv.request.b = 12;
client.call(srv);

## Slide 6: Actions

## Slide 7: Actions: Overview
Actions are like messages and like services
Each action made up of 3 messages:
  Goal, sent by client, received by server
  Result, generated by server, sent to client
  Feedback, generated by server
Non-blocking in client
Allows long-duration activity, with ability to monitor feedback and even cancel before completion

## Slide 8: Actions: Practical Application
Useful for processes that take time
  Moving arm
  Calculate trajectory
Not worthwhile for short information request
  Where is robot
Not appropriate for most sensor data
  What is distance sensor reading
  What is pressure reading
Could be good for closed loop control

## Slide 9: Actions: Lesson 2.2
Create custom action definition
Create action server
Create action client
int32 order
---
int32[] sequence
---
int32[] sequence
SimpleActionClient<FibonacciAction> ac("fibonacci", true);
FibonacciGoal goal;
goal.order = 20;
ac.sendGoal(goal);
void executeCB(const FibonacciGoalConstPtr &goal) { …
if (as_.isPreemptRequested() || !ros::ok()) as_.setPreempted();
as_.publishFeedback(…);
as_.setSucceeded(result_); }
…
SimpleActionServer<FibonacciAction> as_ (nh_, name, boost::bind(&executeCB, this, _1), false);
as_.start();
ros::spin();

## Slide 10: Actions: Lesson 2.3
Fill out a trajectory
Send action to ROS-Industrial robot client
View activity using industrial robot simulator
trajectory_msgs::JointTrajectory trajectory;
trajectory_msgs::JointTrajectoryPoint pt;
trajectory.points.push_back(pt);
actionlib::ActionClient<control_msgs::FollowJointTrajectoryAction>
ac(nh, "joint_trajectory_action");
control_msgs::FollowJointTrajectoryActionGoal goal;
goal.goal.trajectory = trajectory;
ac.sendGoal(goal.goal);

## Slide 11: Message vs. Service vs. Action
Type | Strengths | Weaknesses
Message | Good for most sensors (streaming data) | Messages can be dropped without knowledge Easy to overload system with too many messages
Service | Knowledge of missed call Well-defined feedback | Blocks until completion Connection typically re-established for each service call (slows activity)
Action | Monitor long-running processes Handshaking (knowledge of missed connection) | Complicated Mixed feedback from multiple action servers (not for SimpleAction)

## Slide 12: Launch Files

## Slide 13: Launch Files: Overview
Launch files automate system startup
XML formatted script for running nodes and setting parameters
Ability to pull information from other packages

## Slide 14: Launch Files: Notes
Can launch other launch files
Executed in order, without pause or wait*
  * Parameters set to parameter server before nodes are launched
Can accept arguments
Can perform simple IF-THEN operations
Supported parameter types:
  Bool, string, int, double, text file, binary file

## Slide 15: Launch Files: Lesson 2.4
Basic launch
  Script a list of nodes and parameters
<launch>
<rosparam param="controller_joint_names" >
['joint_s', 'joint_l', 'joint_e', 'joint_u', 'joint_r', 'joint_b', 'joint_t']
</rosparam>
<param name="robot_description“
textfile="$(find motoman_config)/cfg/sia20d_mesh.xml" />
<node name="robot_state_publisher" pkg="robot_state_publisher" type="robot_state_publisher" />
<node name="action_client" pkg="lesson_basic_launch“ type="jointaction_client"/>
</launch>

## Slide 16: Launch Files: Lesson 2.5
Advanced launch
  Include other launch files, even from other packages
  Use arguments to parameterize launch
  Use “if=“ or “unless=“ to do simple control
<launch>
<arg name="robot" default="sia20" />
<arg name="show_rviz" default="true" />
<group ns="robot" >
<include file="$(find lesson)/launch/load_$(arg robot)_data.launch" />
<node name=“state_publisher" pkg="robot_state_publisher“ type="state_publisher" />
<node name=“jt_state_publisher" pkg="joint_state_publisher" type="joint_state_publisher" /> </group>
<node name="rviz" pkg="rviz" type="rviz“ if="$(arg show_rviz)"/>
</launch>

## Slide 17: TF – Transforms in ROS

## Slide 18: TF: Overview
TF used to track all coordinate frames in ROS
Each frame is related to at least one other frame
TF can be used to find transforms between any two relatable frames, even in the past!
TF designed as a distributed network
“A,B”
Frame B
Frame A
Frame C
Frame D
Frame E
“D,E”
“B,C,D”
Transform Between A/E?

## Slide 19: TF: c++
A transformListener listens to all tf messages and tries to determine relative transforms
Can try to transform in the past
Can only look as far back as it has been running
ros::init(argc, argv, "tf_listener");
ros::NodeHandle nh;
tf::TransformListener listener;
tf::StampedTransform transform;
listener.lookupTransform(“target”, “source”, ros::Time(), transform);

## Slide 20: TF: c++
Each robot_state_publisher publishes transforms for a particular urdf
Nodes can also publish /tf data
DANGER! TF data can be conflicting
<launch>
<param name="robot_description" textfile="$(find motoman_config)/cfg/sia5.xml" />
<node name="state_publisher" pkg="robot_state_publisher" type=“robot_state_publisher" />
<node name="joint_state_publisher" pkg="joint_state_publisher" type="joint_state_publisher" />
</launch>
“A,B”
Frame B
Frame A
Frame C
Frame D
Frame E
“D,E”
“B,C,D”
Transform Between A/E?

## Slide 21: URDF: Unified Robot Description Format

## Slide 22: URDF: Overview
URDF is an xml-formatted file containing frames, connections between those frames, and a physical description of a system.
Used for description of everything, not just robots.

## Slide 23: URDF: Link
Each link becomes a frame
Can contain physical information
Frame information is stored in xyz, roll-pitch-yaw format
  Units of meters and radians
<link name="shoulder_link“>
<visual> <geometry> <cylinder length="0.1" radius="0.1"/> </geometry> <origin xyz="0 0 -0.05" rpy="0 0 0" /> </visual> <collision> <geometry> <cylinder length="0.1" radius="0.1"/> </geometry> <origin xyz="0 0 -0.05" rpy="0 0 0" /> </collision>
</link>

## Slide 24: URDF: Joint
A joint connects 2 links
  Contains parent and child frame reference
  Contains transform between parent and child frames
  Types: fixed, free, linear, rotary
  Denotes axis of movement (linear, rotary only)
  Contains joint limits on position and velocity
ROS-I conventions
  X-axis front, Z-Axis up
  Keep all frames similarly rotated when possible
<joint name="shoulder_pan_joint" type="revolute“> <parent link="base_link"/> <child link="shoulder_link"/> <origin xyz="0 0 0.1" rpy="0 0 0"/> <axis xyz="0 0 1"/> <limit lower="-3.14" upper="3.14" velocity="1.0"/>
</joint>

## Slide 25: Contact Info.
Daniel Solomon
Research Engineer
Southwest Research Institute
9503 W. Commerce
San Antonio, TX 78227 USA
Phone: 210-522-3147 Email: dsolomon@swri.org
www.ROSindustrial.org